## Slide 1
Cloud Based Air Pollution Detector
ECE 3100
Electronic Shop Practice

## Slide 2
Outlines
Our Team
Project Overview
Resources
Progress till now
Circuit from Top View
Circuit View on Proteus
Project Demonstration
Statistics
Frontend of Website for statistics

## Slide 3
Our Team Members
Promit Biswas
Roxy Sarkar
1810040
1810039

## Slide 4
Project Overview
It is portable air pollution detector that helps to find out the different air substances level in any specific area and predict future situation and show on a website.
2
3
4
It will detect the amount of AQI, CO, Methane, Butane, CO2, Humidity and temperature appeared in the air.
It will be alarmed when it detects the excessive amount of harmful gases.
The amount of gas particles will be displayed in LCD display.
1
5
It will transfer data to Online Cloud based Website to show data in different times to predict the occurrence.

## Slide 5
Resources
The Resources we used:
LCD Screen
Project Board
Potentiometer
DHT11 Temperature & Humidity Sensor
Wires
Arduino Nano
MQ-135 Gas Sensor
Buzzer
MQ-2 Gas Sensor
MQ-5 Gas Sensor

## Slide 6
This Project can show the Air Substance in PPM values in LCD Display.
Progress
Till Now
READ MORE
This Project can say which ppm is good bad or harmful in display with warning.
Project can individually detect CO, CO2, Smoke, Humidity, Natural gas, LPG.

## Slide 7
Codes

## Slide 8
Circuit From Top

## Slide 9
Circuit
Diagram
On
Proteus

## Slide 10
Project Demonstration

## Slide 11
Levels of Substance
Table of Different Substance
Statistics
Normal Air
With Gas
Burning Papers & Mosquito Coil
CO
CO2
Methane
Butane
AQI
Temperature
Humidity
9 PPM
6 PPM
47 PPM
1 PPM
86 PPM
31 ℃
78%
733 PPM
195 PPM
73 PPM
43 PPM
196 PPM
30.50 ℃
84%
2018 PPM
429 PPM
100 PPM
89 PPM
274 PPM
33.70 ℃
77%

## Slide 12
FrontEnd
WebView
For
Statistics

## Slide 13
Future Scopes
The data collected from any area like RAJSHAHI by this device, will be stored in the cloud.
We will use Bluetooth module to send data to mobile application. From that a text file will be generated automatically and will be uploaded to our website to predict data.
Through the collected data set, by the help of statistics we can forecast about the weather of the specific area and important decisions can be taken on the basis of the collected data and the drawn graph.

## Slide 14
Any Questions?

## Slide 15
Thank You
FOR THE ATTENTION